Integer Division

---
Purpose
1. Verify that the result of the division is correct using a multiply-and-shift operation, representing the divisor with
2. q+ 1 + floor(log2(b))
3. bits instead of sizeof(type(a)) bits, where
4. sizeof(type(a)) ≤ q ≤ nBits(a)
5. And nBits(x) computes the minimum number of bits needed to represent x

---
Multiply-and-shift
You can see the division as
a/d = a*(1/d)= (a*m)>> shift_factor
- sizeof(m) ≤ shift_factor
- Depending on the desired precision shift_factor can change.

---
The previous implementation
1. Compute the multiplier m with sizeof(type(m))≤ shift_factor (i.e at least 32 bits for int…)
2. Compute the division such as result = (a*m) >> shift_factor

---
The improvement
1. Make
2. sizeof(m)= q + 1 + floor(log2(b))
3. Instead of sizeof(m)=sizeof(type(a)).
  In this way it is possible to represent m with few bits respect to the previous implementation.

---
What we want and what we have
1. a is a variable, so we cannot always know nBits(a) at compile time (this is the reason why we use q and not nBits(a) in the formula ). To solve this issue sizeof(m) is computed as
2. min( sizeof(type(a)), minBits )
3. Where minBits = q + 1 + floor(log2(b)). In this way we ensure that we use the minimum number of bits as much as we can.

---
An example 15/3
1. Case 1: we don’t know nBits(15), so we consider that it employs an int size (32 bits).
2. m=286331153110=
3. 101010101010101010101010101010112
4. m is represented using 32 bits.
5. shift_factor = 32+1 = 33

---
Case 1: Result Computation
1. Result = (a*m) >> shift_factor =
2. (15*2863311531)>>33 = 3
4. All in all, we occupied at most 36 bits ( to represent 15*2863311531)

---
Case 2
1. Case 2: we know that nBits(15)=4 bits. This can be done under certain conditions at compile time.
2. m=1110=
3. 10112
  m is represented using 4 bits.
4. shift_factor = 4+1 = 5

---
Case 2: Result computation
1. Result = (a*m) >> shift_factor =
2. (15*11)>>5 = 3
4. This time, we occupied at most 8 bits ( to represent 15*11 ) instead of 36 bits of the Case 1