Multiplication by rational constants

---
Algorithm description
- Input: a small periodic constant a/b, a variable X and the precision w0 of the result
- Output: the result of the multiplication of the variable X for the constant a/b
- How: using shift-and-add tree the multiplication can be done optimally

---
Periodic representation
Transform a/b into a tuple of values:
<e, h, p, s>
Where
- e is the scaling factor exponent, or shift (a/b = x/y*2e)
- h the header, the integer part of the variable (a/b = h + c/d where c/d < 1)
- p the periodic pattern (1/3 = 0.(3)∞ where p = 3)
- s the period size (in bits) of p

---
Periodic representation
Using <e, h, p, s>, we can obtain a/b in this way:
Note that a/b = 2e * (h + c/d)
NB: simplify fraction before generating the tuple

---
Example
70/100 has to be first simplified.
70/100 → 7/10
Then the tuple must be computed
<e = -1, h = 0, p = 6, s = 4>
7/10 = 2-1*(7/5) = 2-1*(0,(01102)∞)
Note that 01102 = 610 = p

---
Building the shift-and-add tree
- To properly compute the multiplication, we have to consider w0 bits of the constant
- Then, we can compute approximations πi of c/d (seen in the previous slide)
First we compute

---
Building the shift-and-add tree
Then we compute better approximations
And in general

---
Building the shift-and-add tree
The computation of πi can stop when
2i * s < w0 ⩽ 2i+1 * s
In this case we can compute j where 0 ⩽ j ⩽ i and being the smallest integer such that (2i + 2j) * s ⩾ w0 – wh (wh being the size of the header h)
In this way, we can use an already computed approximation that is πj to compute the last approximation

---
Building the shift-and-add tree
If h = 0, f is the final result.
Otherwise, we have to add h * x to f.
r = h * x + f

---
Example: x * 1/3 with w0 = 20